The seeker scheduling system – A very rough draft.
Definitions
Performance States: Each DVFS configuration is given a performance state number with 0 being the one with the lowest clock-speed. This is usually denoted as Pn .
T – The total number of performance states supported by the system
N – The total processors on line.
Ci – The i'th processor.
Pi – The i'th performance state. P0 is the one with the lowest clock speed and power consumption, and PT-1 is the one with the highest clock speed and power consumption. Note that this is the exact opposite when compared to P-State provided in processor manuals.
Delta: The total changes in Performance states on a global basis. For example if C0 changes from P2 to P4, and C1 changes from P3 to P0, while all other CPU’s are held at their existing performance state, then the delta of this mutation is said to be |4-2| + |0-3| = 5.
Mutation: The act of changing the performance states of the CPUs in the system.
Mutation Interval: The interval between two consecutive mutations.
Scheduling Quanta: Interval on which scheduling decisions are made. Usually every 1-10ms per processor and depends on the OS configuration.
Layout: The scheduling is done in a hierarchical fashion. A task is given a performance state to execute with which implies a set of processors which are running at that particular performance state. The layout L as seen by the scheduler and the mutator is:
L = left [ matrix{C_{P_0} # C_{P_1} # ... # C_{P_{T-1}} } right ] (scheduler) where C_{P_i} is the set of processors executing in Pi.
L = left [ matrix{ P_{C_0} # P_{C_1} # ... # P_{C_{N-1}} }right ] (mutator) where P_{C_i} is the performance state at which Ci is currently executing with.
For example with T=5, N=4, and C0, C1 in state P0, C2 in state P4 and finally C3 in state P1,
L = left [ matrix{(C_0,C_1) # (C_3) # (%phi) # (%phi) # (C_2) } right ] (scheduler)
L = left [ matrix{P_0 # P_0 # P_4 # P_1 } right ] (mutator)
The indices's are used every time an arithmetic operation has to be performed on the members. For example from the mutator's view, L = [0,0,4,1].
Demand: Number of requests from the previous mutation for each state in the system. It is represented as D = [D0,D1,D2,…]. For example, demand is D = [0,8,8,4,0] implies that from the last mutation, P0 and P4 were never requested, P1 was requested 8 times, P2 was requested 8 times, P3 was requested 4 times.
Introduction

Figure 1: Seeker Scheduler System Architecture.
The performance directed scheduler (PDS) is invoked every scheduling quanta for each and every on line processor and makes decisions of what performance state a task must execute with based on its current performance (derived by reading from the PMU Driver). The information of available states and their comprising CPUs’ (Layout, L) are read in from the Mutation engine. Upon every invocation, the PDS updates the demand array, D with the requested state, and schedules the task on the closest available performance state.
The Delta based Mutation Engine (Mutator), reads in the demand array, based off of which makes decisions on what the new layout must be. The mutator is constrained by delta. If a frequency change is required, the mutator instructs the governor to change and finally, clears the demand array and updates the layout array.
Performance Directed Scheduler:
The performance Directed Scheduler (PDS) is invoked every time a task switch is requested. On a moderately loaded system, this is on an average, every scheduling quanta (1-10ms). Upon invocation, the Instructions per clock (IPC) is computed for the task being switched out from the running state. This is used to make decisions on what performance state the task should execute on. Figure 2 describes the decision diagram. The value chosen for H and L is 0.875 and 0.625 respectively.
All operations performed on the current performance state is adjusted to keep it within bounds [0,T) where T is the total number of states supported by the system. For example, the test machine used for the experiments supports a total of 5 states as shown in Table 1, allowing operations on P to be adjusted to be within [0,5). That is additions performed on P are not allowed to be greater than 4 (T-1) and subtractions are not allowed to be lesser than 0.
State	Frequency	Power Single-Plane	Power - Dual Plane
P0	1100	75	64.6
P1	1400	85.2	75.6
P2	1700	95.4	88.8
P3	2000	106.6	108.2
P4	2200	114.1	115

Table 1: State characteristics for the AMD Opteron 8354

Figure 2: Decision diagram for PDS
This is a simple decision to request for a state one higher than the current state if the IPC was greater than H, by one less than the current state if IPC were less than L. The current state is maintained if the IPC is in the interval (L,H). More information about the procedure used is provided in Figure 3 below.
Figure 3: Scheduling methodology
Example:
Layout chosen by the mutator = [(C0,C1),(),(),(C2),(C3)] (Core 0,1 are in State 0, Core 2 in State 3 and Core 3 in state 4.
Task starts off and runs with an IPC > H, is currently executing with state P0.
Now it requests with state P1 (the left decision arc). But the scheduler notices the layout and that there are no processors currently at P1. Hence it schedules it on the closest P3, and the task migrates to C2. The demand vector is updated to increment the demand for state P1. Note that the demand is updated for the requested state, and not the given state.
On the next reschedule, task has an L < IPC < H, and hence the scheduler requests for the current state P3, and hence continues to execute on C2, and the demand for P3 is incremented.
On the next reschedule, the task has changed phases, and is now executing with an IPC < L, as per the right arc of the decision tree, requests for a state P2 (Incrementing the demand for P2). Upon inspection of the layout, the scheduler chooses P0. And hence migrates to C0 or C1 based on what is loaded the least. Note that PDS does not make decisions on choosing between C0 or C1. That decision is made my the Linux load balancer.
This can be improved by using a delayed adaptive step algorithm shown in figure 3.

Figure 4: Decision Diagram for the adaptive step PDS
Here S is the step size with which the state transition can happen. Thus if S = 2, P = 1 (Current state is P1) and IPC > H, then P = 3 (P3) will be requested while assigning a value of 4 to S.
After the request, an available and unloaded state closest to the requested state is searched in the layout and the task is scheduled on one of the processors executing with the corresponding state. The demand vector is also updated for the requested state.
Note that, the state given to a task and the state requested by a task is dependent on the current layout.
Figure 5: Adaptive Step Scheduling Methodology.

Example. Using the same example, L = [(C0,C1),(),(),(C2),(C3)]
Task starts off executing on P0. The step parameter is currently 0.
First reschedule: IPC > H, PDS requests for state 0 + 0 = P0, (The step is 0). and continues in the same state. The step is updated to be 1. (Second from the left).
Next, IPC > H, Step, S = 1, PDS requests for state 0 + 1 = P1. (Step is 1), and step is updated to be 2. as there are no cpus with P1, task migrates to P3. This is the first decision from the left.
Next IPC > H, State, P3, Step S = 2, PDS requests for state 4 (3 + 2 >= 5, and 4 is the max state number) and finally migrates to P4.
The same goes for all decisions.
Delta constrained Mutation:
Constraint: The total change should be less than or equal to delta.
Optimize: The system tries its best to attain the demand.

Initialization
Compute Delta Matrix M
Compute state weight W
Transition to new state
Adjust Parameters
Delta > 0
Start

End

Figure 6: Delta Constrained Mutation Process.
Each of the subprocesses are described below

Initialization:
Demand vector D updated by the scheduler, is used to compute the number of processors required by each state Pi giving a transformed demand vector d using the Load the system experienced in the elapsed mutation interval. As an optimization to make the system resistant to rapid changes in load, it is computed once every 4 mutation intervals, and utilized as an average.
d_{i} = {D_{i} times Load} over sum from {j=0} to {T} {D_{j}}

Example, if D = [0,12,0,0,8], and the load is 3.0 (3 active processors were used), then d = [0,2,0,0,1] (Make note of the rounded division).
The direction of transition is an indication for the delta matrix on what is the general trend.
Z_R = sum from {i=0} to T {d_i times (i + 1)}
ZR The required Performance

Z_P = sum from {i=0} to N (L_i + 1)
ZP the present Performance

direction, t = left lbrace matrix{ 1 # Z_R > Z_P ## 0 # Z_R = Z_P ## -1 # Z_R < Z_P } right none

The direction of the transition.
Essentially if Direction is 1, then a higher performance is demanded out of the system. -1 implies that a lower performance is required out of the system and a value of 0 indicates that things are fine the way they are.
The Poison Matrix X (N x T matrix) is set to all ones
forall i,j: 0 <= i < N, 0 <= j < T; X_ij = 1
Compute Delta Matrix:
The information in the delta matrix represents the delta constraint and hence mobility allowed for each processor and the preferred direction of transition. Thus as C0 is in state P0, then,with delta = 1, C0 can at most change to P1. In general, this allows a processor to have a preference to stay in its current state or move minimally under the control of the delta constraint.
Based on the current layout and direction, a delta matrix is constructed with each row corresponding to each and every on-line processor, Each column corresponds to each and every available performance state. Essentially, the delta matrix M is a N x T matrix. For a system with 4 cores (C0 through C3) and 5 states (P0 through P4), a matrix shown below is constructed. If Ci is currently in Pj,then it is given a max value of 2T (10 as per this example) which tapers off on either side (Based on direction)for delta number of columns. Beyond which a value of 0 is assigned to the cell expressed by Equation 1-3. L is a vector describing the state each processor is in. So, if C0 through C3 are in states 0,1,2,3, then L = [0,1,2,3]. The delta matrix for each direction possible is shown below. M00 corresponds to processor 0 and state 0. The delta matrix M differs based on the direction required and is shown in equation 1-3 below.
forall i,j: 0 <= i < N, 0 <= j < T; M_{ij} = left lbrace matrix{ 2T # L_i = j ## {T over 2} times (t^2 + t + 2) - abs{L_i - j} # 0 < (j - L_i) <= %DELTA ## {T over 2} times (t^2 - t + 2) - abs{L_i - j} # 0 < (L_i - j) <= %DELTA ## 0 # abs{L_i - j} > %DELTA } right none

Equation 1: Mutation Matrix
Example matrices for L = [0,1,2,3] with each required direction is shown below (delta = 1):
M^+1 = left [ matrix{ 10 # 9 # 0 # 0 # 0 ## 4 # 10 # 9 # 0 # 0 ## 0 # 4 # 10 # 9 # 0 ## 0 # 0 # 4 # 10 # 9 }right ]

M^0 = left [ matrix{ 10 # 4 # 0 # 0 # 0 ## 4 # 10 # 4 # 0 # 0 ## 0 # 4 # 10 # 0 # 0 ## 0 # 0 # 4 # 10 # 4 } right ]

M^{-1} = left [ matrix{ 10 # 4 # 0 # 0 # 0 ## 9 # 10 # 4 # 0 # 0 ## 0 # 9 # 10 # 4 # 0 ## 0 # 0 # 9 # 10 # 4 } right ]

It can be observed that the tapering off is symmetric for M0 while being biased for M+1 where the right leg has a larger value and M-1 where the left leg has a larger value.
Compute state weight:
Elements along each column of matrices M (M+1, M-1 or M0 based on the required direction) are summed and an element by element product with the demand vector d is taken to get the weight vector W. For example, d = [0,2,0,0,1] for state 1, and an upward direction (direction = +1) W2 = 2 x (0+9+10+4)

W_i = d_i times sum from {j=0} to N {M_{ji}}

Equation 5
W = left [ matrix{14 times 0 # 23 times 2 # 23 times 0 # 19 times 0 # 9 times 1} right ] = left [ matrix{0 # 46 # 0 # 0 # 9} right ]
Transition to new state:
p = argmax(W) newline c = argmax(M_ip times X_ip) forall i: 0 <= i < N

Essentially the state with the maximum value in the state weight vector is chosen as the winning state p. Then the element in the column corresponding to state p in the delta matrix times the equivalent element in the poison matrix with the maximum value is chosen as the winning processor.
For example, assuming a delta of 1, and t = 1 with the first iteration, (X is all ones), then
p = 1 with the max value of 46. and the index c = 1 is the one in the corresponding column with a value of 10. So as per this iteration, a transition from state 1 (L1) to state 1 (p) is required for processor 1. Note that as an optimization, a transition is initiated only when L_i != p .

Adjust Parameters:
X_cp = 0 newline %DELTA = %DELTA - abs{L_c - p} newline L_c = p newline d_p = d_p - 1
The value in the poison matrix is set to 0 to avoid the same transition to be initiated which is usually a problem when Lc = p and the use of the poison matrix avoids this condition.
Delta is adjusted to the new value as a transition has been performed.
The layout is updated with the new state value for processor c.
the processor demand for state p is reduced by 1.
Stopping condition:
The process continues for a maximum of load iterations or till delta reaches 0, whichever comes first.