Enabling Dynamic Voltage and Frequency Scaling in Multi-core Architectures
By Amithash Prasad
Under the guidance of
Dr. Connors & Dr. Vachharajani

---
Power Efficient Execution on Multi-core Architectures
Power efficiency is a key problem for modern systems
DVFS has been explored as an effective way of lowering power for single core systems.
Current multi-core systems have per-core voltage supplies each with as many as 5 distinct operation levels
Asymmetric processors complicate the potential of operating system to achieve performance and power efficiency within a system

---
Thesis Statement
This work examines a method for conserving power while limiting the impact on performance to a multi-core architecture by making collective, rather than individual, DVFS decisions.

---
Low IPC
Phased IPC
High IPC

---
Throughput Study

---
Current Methodologies
Phase directed DVFS transitions
Intra-task DVFS
Live Phase monitoring and prediction
Global policies
Workload arrival rate
Per-CPU usage statistics
Utilization ratio of shared resources
None tries to avoid unneeded DVFS transitions

---
Performance Directed Scheduling
H = 0.875
L = 0.625

---
[0004] – astar

---
Mutation Strategy
Demand based mutation
Frequency transitions initiated based on demand of workload
Latency of frequency/voltage transition
Rapid DVFS causes instabilities
Mutation on intervals
Care must be taken to not perform too many transitions
Reuse processors which already exist in the required state

---
Basic Methodology
Quanta
time
Schedule: Assign task to core with the requested/close enough state. Increment demand for the requested state.
Mutation Interval
Mutate: Based on demand, mutate processor P-States to best match the demand.

---
Global P-State of cores
L = left [ matrix{ P_{C_0} # P_{C_1} # ... # P_{C_{N-1}} }right ]
C2 in
P4
C3 in
P1
C0 in
P0
C1 in
P0
L = left [ matrix{P_0 # P_0 # P_4 # P_1 } right ] = left [ matrix{0 # 0 # 4 # 1 } right ]

---
P-State Demand
Scheduler increments Di every time a task requests for state “i”
No usable information
D = left [ matrix{ 0 # 14 # 17 # 1 # 0 } right ]
Query system for the global “Load” - Total active processors in the last interval

---
Processor Demand
Di is incremented for every request for state “i”
d_{i} = {D_{i} times Load} over sum from {j=0} to {T-1} {D_{j}}
D = left [ matrix{0 # 14 # 17 # 1 # 0} right ], Load = 3 newline d = left [ matrix{0 over 32 # 42 over 32 # 51 over 32 # 3 over 32 # 0 over 32} right ]newline d = left [ matrix{0 # 1 # 2 # 0 # 0} right ]
D = left [ matrix{0 # 14 # 17 # 1 # 0} right ], Load = 3 newline d = left [ matrix{0 over 32 # 42 over 32 # 51 over 32 # 3 over 32 # 0 over 32} right ]newline d = left [ matrix{0 # 1 # 2 # 0 # 0} right ]

---
Requested and available performance
Z_R = sum from {i=0} to {T-1} {d_i times (i + 1)}
Z_P = sum from {i=0} to {N-1} (L_i + 1)
d = left [ matrix{0 # 1 # 2 # 0 # 0} right ] newline Z_R = ( 0 + 2 + 6 + 0 + 0) = 8
L = left [ matrix{0 # 0 # 4 # 1} right ] newline Z_P = ( 1 + 1 + 5 + 2) = 9
ZP Present Performance is proportional to 9.
ZR Required Performance is proportional to 8.

---
Transition Direction
t = left lbrace matrix{ 1 # Z_R > Z_P ## 0 # Z_R = Z_P ## -1 # Z_R < Z_P } right none
Transition direction t:
+1 – A higher performance from the system is required
-1 – A lower performance from the system is required
0 – There is a balance between what is required and what is already there.

---
Other initializations
X is the poison matrix of dimensions N x T: Set to all ones. If 0, the transition is avoided
X = left [ matrix{ 1 # 1 # 1 # 1 # 1 ## 1 # 1 # 1 # 1 # 1 ## 1 # 1 # 1 # 1 # 1 ## 1 # 1 # 1 # 1 # 1 } right ]
Δ – Constraint on mutation
δ – Constraint on the mutation
      in this interval
%delta = %DELTA

---
Delta Matrix
%DELTA = 2, %delta = 2 newline L = left [ matrix{0 # 0 # 4 # 1 } right ]
C0
C1
C2
C3
M^{t = +1} = left [ matrix{ 10 # 9 # 8 # 0 # 0 ## 10 # 9 # 8 # 0 # 0 ## 0 # 0 # 3 # 4 # 10 ## 4 # 10 # 9 # 8 # 0 } right ]
P0 P1 P2 P3 P4

---
Start: Delta Matrix M
M^{t = +1} = left [ matrix{ 10 # 9 # 8 # 0 # 0 ## 10 # 9 # 8 # 0 # 0 ## 0 # 0 # 3 # 4 # 10 ## 4 # 10 # 9 # 8 # 0 } right ]
M^{t = 0} = left [ matrix{ 10 # 4 # 3 # 0 # 0 ## 10 # 4 # 3 # 0 # 0 ## 0 # 0 # 3 # 4 # 10 ## 4 # 10 # 4 # 3 # 0 } right ]
Based on t, the delta matrix is different.
t = +1, favor transition to higher state
t = -1, favor transition to lower state
t = 0, take no sides.
M^{t = -1} = left [ matrix{ 10 # 4 # 3 # 0 # 0 ## 10 # 4 # 3 # 0 # 0 ## 0 # 0 # 8 # 9 # 10 ## 9 # 10 # 4 # 3 # 0 } right ]

---
Delta Matrix M (Formal definition)
forall i,j; 0 <= i < N, 0 <= j < T, M_{ij} = left lbrace matrix{ 0 # j < (L_{i} - %delta) ## {T over 2} times (t^{2} - t + 2) + j - L_{i} # (L_{i} - %delta) <= j < L_{i} ## 2T # j = L_{i} ## {T over 2} times (t^{2} + t + 2) - j + L_{i} # L_{i} < j <= (L_{i} + %delta) ## 0 # j > (L_{i} + %delta) } right none

---
State Weight
X = left [ matrix{ 1 # 1 # 1 # 1 # 1 ## 1 # 1 # 1 # 1 # 1 ## 1 # 1 # 1 # 1 # 1 ## 1 # 1 # 1 # 1 # 1 } right ]
W_i = d_i times sum from {j=0} to {N-1} {M_{ji}}
p = argmax(W) newline c = argmax(M_ip times X_ip) forall i: 0 <= i < N
M^{t = -1} = left [ matrix{ 10 # 4 # 3 # 0 # 0 ## 10 # 4 # 3 # 0 # 0 ## 0 # 0 # 8 # 9 # 10 ## 9 # 10 # 4 # 3 # 0 } right ]
c = 2
p = 2
d = left [ matrix{0 # 1 # 2 # 0 # 0} right ]
W = left [ matrix{0 times 29 # 1 times 18 # 2 times 18 # 0 times 12 # 0 times 10} right ] = left [ matrix{0 # 18 # 36 # 0 # 0} right ]

---
Adjust Parameters
d_p = d_p - 1 newline d_2 = d_2 - 1 = 2 - 1 = 1
%delta = %delta - abs{L_c - p} = 2 - abs{4-2} = 0
Adjust Iteration delta constraint
Adjust processor demand, we just
Satisfied one.
X_{cp} = 0 newline X = left [ matrix{ 1 # 1 # 1 # 1 # 1 ## 1 # 1 # 1 # 1 # 1 ## 1 # 1 # 0 # 1 # 1 ## 1 # 1 # 1 # 1 # 1 } right ]
Continue till iteration delta constraint is 0, or we have performed “load” number of iterations.
Adjust Poison matrix

---
Methodology Overview
Quanta
time
Schedule: Assign task to core with the requested/close enough state. Increment demand for the requested state.
Mutation Interval
Mutate: Based on demand, mutate processor P-States to best match the demand.

---
Power/Performance: Workload

---
Mutation Method Showdown
Delta Mutation
Ondemand mutation
Conservative Mutation
Error in slowdown measurements is:
+/- 10%

---
Parameter Space Exploration: Delta and Mutation Interval

---
Medians of Slowdown and performance savings
Mutation Method	Median Slowdown %	Median Power Savings %
Delta constrained mutation Delta = 4	16.45	32.48
Ondemand Mutator	0	21.8
Conservative Mutator	0	21.79

---
Source Code
git clone git://github.com/amithash/seeker-scheduler.git

---
Thank You
Questions?